Simple j-pole antenna for 2 meters using 450 ohm ladder line

1. Measure out and cut about 59 or 60 inches of ladder line.

2. Strip both ends (top and bottom) about an 1/2 to 3/4 inch and bend each toward the center so they will overlap each other.

3. After you overlap the wire, measure the entire length of the antenna. Your shooting for 58 inches total length after stripping and overlapping the wires.

4. After achieving your 58 inches (give or take a half inch), solder both ends.

5. Determine which end has the solid plastic closest to end and put a hole through it so you'll have some way of hanging the antenna. (cable tie)

6. On the opposite end (bottom end), measure up 19 inches from the actual bottom (where wires are overlapped), and cut out a 1 inch gap of 1 wire from one side only leaving the gap. You should end up with a very thin slim rectangle from top to bottom with a 1 inch gap starting at 19 inchs up from the bottom on one side only.

7. Have an rg58 or rg8x pigtail made with a pl259 on one end and shield and center wire tinned with solder on the other end.

8. Measure up about 4 inches from the bottom and remove the insulation from each side of the Slim Jim antenna using the 4 inch measurement as your center point and remove the insulation about 2 inches up and down from the 4 inch mark to give you access to the conductors on each side of the antenna for swr tuning. 

 9. Connect center conductor to the long side and shield to short side in a temporary fashion. (I used crimp connectors bent on the end of the pigtail which would connect around the each wire of the antenna for testing).

10. Using 2 or 3 plastic cable ties, wrap them around the antenna and pigtail so they will be parallel and snug and to reduce strain on the soldered connection.

12. Approximately 1 foot down on your coax make a choke by looping 5 turns of coax into an approximate 4 inch loop. Using electrical tape secure the loop turns. This J-pole is a balanced antenna going into an unbalanced feed line and can cause RF to get back into the Rig and into the shack. Always remember this step to protect yourself and equipment.