Winlink Operational Screen Settings

Summation of information from myself & others by

WA9APQ 10/14/18

Standardize SSID: No dash is keyboard to keyboard, -1 through -5 is a node (-1 being first), -7 is packet PBBS, -10 is RMS gateway, -11 is Chat, -6, -8, -9, -12 through -15 are unused but open

Both stations who are sending/ receiving peer to peer must have open session screen open and sender must have the receiving stations call sign shown on the screen. Also, both stations must have the identical center frequency typed into the proper screen box. The dial frequency will self populate.

HF using RMS, CMS

Main screen: 		Winmor Winlink

Message screen:	From WA9APQ, Winlink Message, Post to Outbox

Open Session screen:	Have already switched to Winlink Session, KA9$JZ, 3571.5, 3570.0, START

HF Direct (peer to peer) Winmor

Main screen:		Winmor P2P

Message screen:	Peer to Peer Message, Post to Outbox

Open session screen:	Have already switched to Winmor Peer to Peer, KA9$JZ, choice of RMS frequency, START

HF Direct (peer to peer) Ardop

Main screen:		Ardop P2P

Message screen:	Peer to Peer Message, Post to Outbox

Open session screen:	Have already switched to Ardop Peer to Peer, KA9$JZ, choice of RMS frequency, START

VHF using RMS, CMS

Main screen:		Packet Winlink

Message screen:	From WA9APQ, Winlink Message, Post to Outbox

Open session screen:	Have already switched to Winlink Session, DIRECT, KB9G%-10, START

Anytime the internet is addressed, use WINLINK PACKET.

VHF direct (Peer to Peer)

Main screen:		PACKET P2P

Message screen:	From WA9APQ, Peer to Peer, Post to Outbox

Open session screen:	Have already switched to Peer to Peer session, DIRECT, KA9$JZ, START

Set PACLEN at 128 or less. Keep deviation at 5 kcs or less, never more, preferably 3.0

In peer to peer, when using Direct, Digipeater, or Script: Set Main screen to Packet P2P; Message screen to Peer to Peer;

DIRECT:  Open Session screen to Packet Peer to Peer, DIRECT, KA9$JZ

DIGIPEATER: Open Session screen to Packet Peer to Peer, DIGIPEATER, KA9$JZ via W9$TK, k9%UL

SCRIPT: Open Session screen to Packet Peer to Peer, SCRIPT

Then write a script by ADD SCRIPT. Name it W9$TK. Type:

c W9$TK-2           (enter)

conn                 (enter)

(enter)

(enter)

c K9%UL-1           (enter)

conn                  (enter)

(enter)

Add additional stations as necessary as shown above, but be sure the SSIDs are all correct for what you are trying to do. Push SAVE at top of page. Several scripts can be written and saved. Simply click on the appropriate one for your path.

Close session, open session, wait for ready, Push START, watch the steps as the packet moves through the system.